## Slide 1: Arduino Class Programming with Examples
Part 2: Code Review & Demo
Alan Lomax
M8640
Notes: MERG presentation for the Arduino SIG. Prepared 2nd half of 2021 for presenting when needed.
Made into a 2 part presentation to allow time for a show and tell session in part 2.
Presented January 2022.

## Slide 2: About Me
Alan Lomax
calls Ontario, Canada his home
Notes: As mentioned last time I am not a professional programmer but I always like learning new things.

## Slide 3: Introduction
Notes: Me at Widnes shed circa 1964

## Slide 4: Agenda
Recap from Part 1
The all in One Approach
Moving Forward
Detour => Organizing Files
Inspecting the Led2 Class in Detail
Live Demo
Questions
Backup Material
Notes: This is the second part of a chat about software Classes.
- In the first part we develop the general concepts … look at some code fragments to understand how they work … but not in great depth.
- In todays second part we will go through a complete example … with some live demonstration of class programming.
- Agenda Review

## Slide 5: Recap from Part 1
Part 1
Back to Agenda

## Slide 6: Part 1 (In one Page)
Bread and butter- Basic variable types like bool, int, and string.
A struct{} can be considered as a custom variable type
Creating a Class{} is also defining a custom variable type.
We looked at some code fragments to hopefully get a feel for what is going on inside the shoebox. The constructor function creates our objects. Other member functions allow us to interact with that object.
Reusability of a class without exposing the complexity makes for significant coding efficiency. This applies to both writing, comprehending, and maintaining our code.
There can be private and public members of a class. (These can be member variables or member functions). I used the analogy to a shoebox frequently. Some things are hidden inside the box, but some other things are visible on the outside. To just use a class you do not need to know the insides.
Notes: Summary of what was covered in part 1
Getting reacquainted with the vocabulary

## Slide 7: Our Sketch
#include “Led2.h”
Led2
Class Definition
#include "Led2.h"
Led2 myLed1 = Led2(13);
So we can use this line to create a new object.
The header lets our sketch and the compiler know how to use the Led2 class to make a new object
Name of our New Object
Constructor with a passed parameter to be used when first constructing the object
Notes: Building on Part 1 material this is our sketch as it was introduced last time.
At the moment we are chatting about using the class …. Not about writing the class definition. (cover writing the class later)
This is a typical style – but by no means the only way of doing it.
First: What does the #include line do ?
It is what is called a compiler directive – it is not something that ends up in your code after it is compiled – but it does tell the compiler to do something.
When the compiler gets to the #include line it goes out and reads that file and inserts right then and there and then continues compiling starting with the first line of the header file.
This NOT unique to classes and this behavior is used frequently on software projects where code is shared.

## Slide 8: The All in One Approach
Part 2
Back to Agenda

## Slide 9: A Typical File Arrangement
Sketch
Header File
CPP File
#include header File
#include header File
Matched
Set
A Best Practice: The two files are a matched set and named the same as the class
Led2.h and Led2.cpp is my example.
Notes: Last time I assumed this mental model .. And conveyed it as such .. But left it dangling a bit at the end.
I need to bring in some terminology which we will go into in more depth later.
“The Sketch” is most definitely outside of the shoebox. No hidden complexity is visible here.
The Header File – defines private and public variables and has ‘prototypes’ for functions – more on prototypes later
The CPP file – is also called an implementation file – it has the code that implements the functions that we need
This file organization is commonly used for ANY shared code – (with or without classes).
Header file and implementation file are normally a matched set. (matched by naming and the contents)
I had assumed this mental model because I was developing with my library in mind
I knew where the header and implementation file were going to go.
However … you could put all three of these code bits into one larger file … next page.

## Slide 10: All in one View
Sketch
Class Header ‘Code’
Class Implementation ‘Code’
A Quick Show and Tell - of all in one code. (MERG Demo 0a)
A single .INO file
Notes: In the all in one approach the same elements we just talked about are all there .. (We just don’t need the #include lines)
This is an excellent approach as you are writing a new class for the first time.
No need to juggle multiple files – no concerns about other users.
Once the code is mature then carve it out and make up the separate files – this is trivial to do.
This is an early test of my setup – second web camera and also sharing the Arduino IDE.
Don’t want to go too deep explaining code here – we will cover it more later on.
Point out key terms:
Point out private and public sections, a private function init()
Explain the ‘scope operator’ ::

## Slide 11: Summary
The class code does not need to be separate.
You could put class code right in your sketch and then there is only one file to maintain.
But lose a key advantage – libraries and code sharing
And a big drawback is that the hidden complexity is now back in plain view.
It is not typical to put your final class code in one file but it can be done and is perfectly fine for development work.
Notes: Putting all of the code in one file is convenient for first time development work.
Knowing when to split it into separate header and implementation files is a matter of judgement.
There is no right or wrong answer.

## Slide 12: Moving Forward
Part 3
Back to Agenda

## Slide 13: Typical File Arrangement
Sketch
Header File
CPP File
Create and use classes
Define types and what functions are available.
#include header File
#include header File
Implement the functions
Notes: Same picture as was shown before but explains what the files do.
Header file defines types such as user defined classes ;
Also defines function signatures, i.e. what parameters the function uses (with types) and what type it returns.

## Slide 14: Header File
Declares the private and public member variables and functions for our class
Each function is declared with its name and its prototype.
Prototype = A strict definition of passed variable types, their order, and also the returned variable type. This is very important so the compiler knows later on (in your sketch) what is a expected for that function call. Programmers will refer to the ‘signature’ of the prototype – another way of saying it’s uniqueness.
We will see later my Led2 class has two constructors (with different signatures). Note: when you have several function declarations with the same name but where the parameter types are different it is called overloading the function. As long as each call has a distinct ‘signature’ this is ok.
The header could also implement functions (inside or outside of the class). Even though style guides may frown at it … it can still be done.
Here is one Line from the header file:
void onTime(long on); // Set the onTime to a new value
Notes: To some extent it is a matter of programming style –
There are pros and cons to the various ways and I am definitely not an expert on it.
The grey box shows one line from the header file – the line is called a prototype for the indicated function.
Notice – NO curly braces, ends in a semi colon.
The name of the passed variable (‘on’ in this case) is actually ignored in the prototype
It is the # of variables the order, and their types that are important. (the signature)

## Slide 15: The Header File
- a header file (*.h) and
- a C++ program (*.CPP)
{ snip }
/*****************************************************
** Led2_H **
** **
** This class implements standard LED on-off **
** logic on a pin you specify plus a configurable **
** blinking effect. It does so without any delay **
** calls. (no blocking code) **
*****************************************************
*/
class Led2 {
private:
int _pin; // the number of the LED pin
unsigned long _onTime; // milliseconds of on-time
unsigned long _offTime; // milliseconds of off-time
unsigned long _nextTime; // next time change in milliseconds
bool _blink; // true if we are in blinking mode, false if not
{ snip }
public:
Led2(byte pin); // Prototype for simple constructor
void update(); // update things based on elapsed time (call often)
void off(); // Turning off the LED (and sets blink to false)
void on(); // Turning on the LED (and sets blink to false)
{ snip }
};
Tell compiler we are defining a class
Some member variables (or member functions) are private
(completely inside the shoebox)
Some are public – available outside the class (They stick out of the shoebox)
Notes: We covered some of this last time but I am building up and reinforcing the vocabulary.
Notice the header has no real executable code of its own – only variable and function declarations
For the functions the lines in the header file are called the prototypes. Each prototype has a distinct signature.
Mention “The Signature” which must match perfectly between header file and the cpp code
Type signature is the type of the returned variable plus the number and type of the passed variables.
The actual variable name in the prototype is irrelevant and need not even be present.
Remember the constructor? It is the member function that has same name as class and no other return type

## Slide 16: The C++ Program file ( *.cpp)
Implements the member functions for our class.
Each function call was precisely identified in the header by a prototype having the same signature
void Led2::onTime(long on) { // update the desired on time of the led
_onTime = on;
}
Notes: The grey box is showing the code that implements the onTime function.
Passed and returned variable types are strictly according to the prototype.
Note: curly brackets (prototype did not have any)
The actual name of the passed variable is of course NOT ignored here .. Since your function code likely will be using it.
My coding style – all internal (private variables) are named with a leading underscore just for clarity)

## Slide 17: The C++ part
- a header file (*.h) and
- a C++ program (*.CPP)
#include "Led2.h"
Led2::Led2(byte pin) {
// Save the passed pin
_pin = pin;
init();
}
void Led2::init() {
pinMode(_pin, OUTPUT); // define our output pin
off(); // call the function that sets our LED to off initially
}
void Led2::off() {
_blink = false; // Turn off blink mode
_state = LOW; // Set the desired state - LED will turn off on next call to update
}
void Led2::on() {
_blink = false; // Turn off blink mode
_state = HIGH; // Set desired state LED will turn on with next call to update
}
void Led2::update() {
if (_blink) { // If in blinking mode look at timing first
if ( millis() >= _nextTime) { // It is time to do something.
_state = !_state; // swap states
_nextTime = millis() + (_state == HIGH ? _onTime : _offTime); // and calculate when next
// change of state is due
}
}
digitalWrite(_pin, _state); // update the actual output according to desired state
}
Led2 myLed1 = Led2(13);
myLed1.on();
myLed1.update();
myLed1.off();
Notes: Slide build up:
Include the header
CONSTRUCTOR (name is same as class name). We pass it a pin #)
  all it does is save it in a private variable called _pin
  Then call a separate function to initialize things.
The double colon ( :: ) is called the ‘scope operator’. It tells the compiler (and us) that the name on the right is within the scope of the name on the left. This prevents naming conflicts between what is inside the shoe box and what is outside the shoebox. It is a little confusing for the constructor where the CLASS name (left side) is the same as the Constructor (right side) But it is easier to see the usage on other member functions.
The separate member function to initialize things is itself dirt simple .. It sets the pinMode and calls yet another member function called off().
The separate member functions on() and off() just set two internal member variables. Note that at no point so far have we actually written anything to the output.
The Magic Sauce. Is a public method called update. We will go through it line by line on the next slide.
The term member is used to indicate that these items are part of the class definition and not normal everyday code.
A member variable or a member function is implemented inside the shoe box. But if it is public – it can be called from outside.
Most of the methods (or functions if you prefer) just get or set internal variables. In quick and out.
The update method reads and acts on the internal variables
In the code I am showing the update function is doing most of the work but again it is quick – get in and get out.

## Slide 18: The Magic Sauce: the update() method
Led2 Class
“update” method
myLed1.update(); // update the myLed1 object
void Led2::update() {
}
digitalWrite(_pin, _state); // update the actual output according to desired state
if (_blink) { // If in blinking mode look at timing first
}
if ( millis() >= _nextTime) { // It is time to do something.
}
_state = !_state; // swap states
_nextTime = millis() + (_state == HIGH ? _onTime : _offTime); // and calculate when next
// change of state is due
output
_pin, _blink, _state
Notes: Most of this is review from last time – getting reacquainted with the terminology.
Talk it through as text box builds up in several stages.
Be sure to differentiate between the class definition (the pastry cutter) and the specific object (the mince pie)
Could review the calculation of _nextTime which uses ternary operator (three variables) … aka conditional evaluation

## Slide 19: The Sketch
#include “Led2.h”
Led2 myLed1 = Led2(13);
void setup() {
myLed1.onTime(50); // Set LED onTime (50 ms)
myLed1.offTime(300); // Set LED offTime (300 ms)
myLed1.blink(); // turn on blink mode
}
void loop()
{
myLed1.update(); // call update frequently
}
Defining it before setup makes myLed1 a global variable. It can be accessed in setup or in loop code.
In setup configure any settings we want.
Loop code could not be simpler. The work is done inside the class checking millis() and doing the work.
Notes: Come back to our sketch
The blue is the Class name
Our object is in green
The dark red are member functions .. And the first one is the ‘constructor’
We did not talk about onTime and offTime but as you would expect they just save the passed values into private variables inside the class.
The update function will examine those internal variables to see if it is time to do something.

## Slide 20: Detour => Organizing files (*.h and *.cpp)
Part 4
Back to Agenda

## Slide 21: File Locations
Parrot_Sketch.ino
Option #1
Option #2
Parrot_Sketch.ino
Led2.h
Led2.cpp
Led2.cpp
Led2.h
// In Parrot_Sketch.ino use quotes
#include "Led2.h"
// In Parrot_Sketch.ino use angle brackets
#include <Led2.h>
Notes: Using double quotes ("") causes it to search the current working directory and only if that search fails the default include directory.
If you use quotes … and the files exist in both places … it is easy to get yourself confused about which files to edit. (how do I know?)
If you use <angle brackets> then the two files must go in your libraries folder (under the folder where you keep your sketches.)
The first is good for code under development .. The second is good for your final code – other sketches can just use it by including it..
Within libraries can have as many subfolders as you like - It would be a good idea to put the two Led2 files in their own subfolder
Take a look at IDE again
Option 1 is good for developing class programs. (all files are visible withing the IDE – compile errors will give warnings)
Option 2 is good when the code is ‘stable’ – many sketches can share the class without having lots of copies floating around

## Slide 22: In the IDE: To Find Your Sketch Location
While looking at preferences for file location:
Here is File Location (and therefore Library Location)
Check Compiler warnings – set to ‘ALL’ vs default of ‘none’
Turn on ‘Display line numbers’ – makes finding things much easier.
Notes: In Arduino IDE
File – Preferences and take note where your sketches are kept
When you go to that folder you should see the subfolder inside it called libraries
Inside there will be all the libraries you have downloaded – Adafruit, Arduino and others.

## Slide 23: Inspecting the Led2 Class in detail
Part 5
Back to Agenda

## Slide 24: The full Led2 class
offTime (ms)
getBlink (T / F)
Led2 Class
Output (Pin)
“on” Command
“off” Command
On and Off commands are hardly a compelling usage case
“blink” Command
“onTime (ms)”
“offTime (ms)”
getState (T / F)
A blink command for our class makes it a bit more interesting
“update()”
Set and read back user definable on time and off times – even better
Blinking an LED output without ever calling delay() is an example of hidden complexity
As a user you don’t need to know how it works, only that it does work!
Code comprehension is almost intuitive.
“update()”
Complexity is hidden inside the shoebox
onTime (ms)
myLed1.on();

## Slide 25: Led2.H
#ifndef MY_LED2_H
#define MY_LED2_H
#include "Arduino.h"
/*
*****************************************************
** LED2_H **
** **
** This class implements standard LED on-off **
** logic on a pin you specify plus a configurable **
** blinking effect. It does so without any delay **
** calls. (no blocking code) **
*****************************************************
*/
class Led2 {
private:
int _pin; // the number of the LED pin
unsigned long _onTime; // milliseconds of on-time
unsigned long _offTime; // milliseconds of off-time
unsigned long _nextTime; // next time change in milliseconds
bool _blink; // true if we are in blinking mode, false if not
int _state; // ledstate used to set the LED
void init(); // Initialization code
public:
Led2(byte pin); // Prototype for simple constructor
Led2(byte pin, unsigned long on, unsigned long off); // this constructor includes the on and off time values
void update(); // update things based on elapsed time (call this as often as possible)
bool getState(); // Return the current state of LED (on / off)
bool getBlink(); // return the LEDs current blinking state (true / false)
void onTime(long on); // Set the onTime to a new value
long onTime(); // Return the current onTime
void offTime(long off); // Set the offTime to a new value
long offTime(); // Return the current offTime
void off(); // Turning off the LED (sets blink to false and ignores timing values)
void on(); // Turning on the LED (sets blink to false and ignores timing values)
void blink(); // set the LED to a blinking state using the previously set timing values
};
#endif
These two lines are called an #include guard.
They prevent including the same code twice.
First line - IF NOT DEFINED (name)
Second line – DEFINE (name)
At end of the header file – END IF
An alternate: at top of file put #pragma once
(less confusing, less prone to error)
Notes: Full Code of Header
Explain pros and cons of #pragma once (even when copied and pasted it still works)
With the traditional guard approach a copy /paste will fail if you do not rename the ‘variable’ you are defining.
And the error messages that result might not point directly back here!

## Slide 26: Led2.CPP (1/3)
#include "Led2.h“
Led2::Led2(byte pin) { // simple constructor
_pin = pin; // Save the passed pin
init();
}
Led2::Led2(byte pin, unsigned long on, unsigned long off) {
// Save the passed pin and timing values into the equivalent local variables (with underscore)
_pin = pin;
_onTime = on;
_offTime = off; // Initializing code is kept separate just for clarity.
init();
}
void Led2::init() {
pinMode(_pin, OUTPUT); // define our output pin
off(); // call the function that sets out LED to off initially
}
Notes: Full Code of Class Program . Talk it through.
This is showing the ‘constructors’ (plural)
Two different signatures – saving a few lines in our sketch.
Separate init() code allows calling it twice (or more) without needing to repeat the code.
I think in general it is a good practice is to minimize repetition of code – use standalone functions and call them as needed.

## Slide 27: Led2.CPP (2/3)
void Led2::update() {
if (_blink) { // If in blinking mode look at timing first
if ( millis() >= _nextTime) { // It is time to do something.
_state = !_state; // swap states
_nextTime = millis() + (_state == HIGH ? _onTime : _offTime); // and calculate when next
// change of state is due
}
}
digitalWrite(_pin, _state); // update the actual output according to desired state
}
bool Led2::getState() {
// return the current state of the led (True or False)
return _state;
}
bool Led2::getBlink() {
// return the current blink state of the led (True or False)
return _blink;
}
Notes: Full Code of Class Program
Talk it through.

## Slide 28: Led2.CPP (3/3)
void Led2::onTime(long on) {
// update the desired on time of the led
_onTime = on;
}
long Led2::onTime() {
// return the current on time of the led
return _onTime;
}
void Led2::offTime(long off) {
// update the desired off time of the led
_offTime = off;
}
long Led2::offTime() {
// return the current off time of the led
return _offTime;
}
void Led2::off() {
_blink = false; // Turn off blink mode
_state = LOW; // Set the desired state - LED will turn off on next call to update
}
void Led2::on() {
_blink = false; // Turn off blink mode
_state = HIGH; // Set desired state LED will turn on with next call to update
}
void Led2::blink() {
_blink = true; // Turn on blink mode
_nextTime = millis() + _offTime; // Next change of state will be when the off time has expired
}
Notes: Full Code of Class Program
Talk it through.

## Slide 29: Live Demo
Part 6
Back to Agenda
Notes: A few demos coming up.
I will share and wink over to Arduino IDE
Stop sharing and switch cameras to look down the Arduino.

## Slide 30: Live Demo Time
Single LED blinking ( MERG_DEMO1a)
Multiple LEDs blinking with very different timing patterns ( MERG_DEMO2)
Multiple LEDs blinking and a Servo sweep ( MERG_DEMO3)
Notes: Share screen show code … load code wink over to second camera describe what people are seeing.
Change timing and show effect. Pause for discussion.
Point out how class header and cpp files are visible in the IDE as tabs
Look into class code – discuss how it is working as our sketch code flows through the lines.

## Slide 31: Summary: How it all works together
1) Use The class definition and create an object like so:
Led2 myLed1 = Led2(13);
2) constructor runs and sets private (internal to class) variables:
_pin = 13, _state=OFF
and the mode of _pin is set to OUTPUT
Led2
Class Definition
output
on
off
update
Object
myLed1
_pin = 13
_state = OFF
pinMode(_pin, OUTPUT);
13
on
off
update
5) When next our loop code calls myLed1.update() it will check the local variables _state and writes it to the output pin.
It is only at this point our LED will turn ON.
Object
myLed1
_pin = 13
_state = ON
13
on
off
update
4) Now lets say we called the on method myLed1.on() All this does is set the local variable _state to on. At this point still nothing happens because _state is just a private variable inside our class.
3) In loop code we call the update method myLed1.update() which executes the line digitalWrite(_pin, _state)
Not too much else happens- we just turned off a pin that was probably already off!

## Slide 32: Recap
A user defined variable type
A blueprint for making software ‘objects’
Hides complexity, increasing code comprehension
Coding productivity in new programs
Improved software maintainability
A fundamental part of Object Oriented Programming

## Slide 33: Led3: New and Improved
No changes to the existing Led2
But development has continued with Led3
Notes: My class code development has not been sitting still.
This presentation has been in the works for more than six months.
I did not want make disruptive changes to Led2 and will keep it around as a companion to this presentation.

## Slide 34: The full Led3 class
offTime (ms)
getMode ()
Output (Pin)
“on()”
“off()”
“setMode()”
getState (T / F)
“update()”
onTime (ms)
enum mode {
Normal,
Blink,
Random,
Flicker,
Welding
};
“configMode()”
Output2 (Pin)
Led3
Define a Led3 variable as before (with a pin #)
New:
Call setMode( newMode )
Can then configure each modes properties
Notes: Normal – call on and off for led operation
Blink – configure on time and off time
Random – configure minimum and maximum on time and off time but actual time is random
Flicker – configure a flickering candle effect – using timing and intensity
Welding– configure a welding effect similar to flickering candle effect and random mode together. Also with second led for an afterglow effect.

## Slide 35: Led3 Modes
Normal – (the default) Just call on() and off() for standard led operation
Blink – configure on time and off time
Random – configure minimum and maximum on time and off time but actual time is random
Flicker – configure a flickering candle effect – using timing and intensity
Welding– configure a welding effect not unlike a combo of flickering and random together. Also with second led for an afterglow effect.

## Slide 36: Led3: Demonstration ?
Parrot_Sketch
it’s not dead yet!

## Slide 37: Other Classes You Can Review / Use
DblDelay https://github.com/Alan-Lomax/DblDelay
Timer https://github.com/Alan-Lomax/Timer
Button https://github.com/Alan-Lomax/Button
LCD2x20 https://github.com/Alan-Lomax/LCD_NHD2x20
Led2 https://github.com/Alan-Lomax/Led2
Top Level (in case of more examples) :
https://github.com/Alan-Lomax
Notes: Can take a look at and talk through the code

## Slide 38: Questions?
Part 7
Back to Agenda
Additional Backup Material Follows

## Slide 39: Backup Material
Part 8
Back to Agenda

## Slide 40
References and Additional Material
Binary numbers and types :
https://learn.sparkfun.com/tutorials/data-types-in-arduino/all
http://users.ece.utexas.edu/~valvano/embed/chap3/chap3.htm
Arduino Compiler / Preprocessor Directives
https://www.deviceplus.com/arduino/arduino-preprocessor-directives-tutorial/
Multi-Tasking on the Arduino:
    https://learn.adafruit.com/multi-tasking-the-arduino-part-1/overview
Conditional Evaluation (ternary operator):
  https://www.tutorialspoint.com/cplusplus/cpp_conditional_operator.htm
Alternate explanations on the subject of Classes:
https://www.guru99.com/cpp-classes-objects.html
https://www.geeksforgeeks.org/c-classes-and-objects/
http://paulmurraycbr.github.io/ArduinoTheOOWay.html
Common Mistakes and How to Fix them:
https://www.acodersjourney.com/top-10-c-header-file-mistakes-and-how-to-fix-them/

## Slide 41: Lessons Learned
IMO: The hardest part is knowing what properties and methods are available with a (non-trivial) class.
Not only what they are but also the many options available for a given property can also be quite involved.
These aspects are often poorly documented. Realizing the true power of a class is a challenge under such conditions and users might be reluctant to accept the implementation at face value.
An example sketch demonstrating usage of some properties is helpful – but is not sufficient especially if there are many options and alternate uses.

## Slide 42
Back to Agenda
End of Presentation

## Slide 43
The Next Train Departs in:
Notes: Using this PowerPoint break timer
This PowerPoint slide uses images, custom animation, and timing to provide a countdown timer that you can use in any presentation. When you open the template, you’ll notice that the timer is set at 00:00. However, when you start the slide show, the timer will start at the correct time and count down by 1-minute intervals until it gets to 1 minute. At that point, it will count down in two 30-seconds intervals to 00:00.