## Slide 1: Practical Arduino
From the Ground Up

## Slide 2: Outline (assumes no Prior electronics or Arduino knowledge)
Review Design Objectives. What you will learn. What you will need. Primer on Components and Symbols. Conductors, Insulators and Ohms Law. Introduce the kit and the included parts and how to obtain one.
Schematic vs PCB. Start it simple. Work up to this design complete walkthrough. (parts orientation, details, tips and tricks, how to solder, assemble board.) Build up the power supply portion the board. How to test your work with visual inspection and basic electrical testing.
Finish the build. Introduce The Arduino IDE. Use of in built test programs like Blink, Servo etc
More on Arduino IDE and simple program design. Use of serial monitor for debugging. Examples of practical use (Each as a standalone short video)
  LED outputs (timing and random light)
  Button Inputs (debouncing and controlling program flow)
  Infrared detectors (sensor needed)
  LDR sensors (LDR needed)
  Motor Control (Motor Shield needed)
  LCD displays (LCD display needed)

## Slide 3: General Requirements
Basis:
An Arduino based hardware and software project that will serve as a learning platform
Finished product would be very useful in a variety of situations on any layout.
Ideally ordered as a complete kit. (PCB, all components, including Arduino NANO (clone))
Detailed instructions suitable for novices. Broken down as ‘build’, ‘test’, ‘learn’.
A series of videos can be made for self paced learning (able to pause, go back, review and check)
PCB design should be flexible in that I/O can be reconfigured without too much fuss. (for example taking the LED’s off board)
No expectation of ‘live sessions’ other than maybe introducing the kit once it is available
NANO V3 MCU
Carrier Board
4 LED on board via R680
2 SERVO via 3pin Header
I2C via A4/A5
2 Buttons on board
DCC signal via optocoupler
4 Sensors via 3 pin header
AC/DC or DCC powered
ULN2803A Output Driver
Feature List:
Socketable NANO on a carrier board.
Carrier board itself to have mounting holes.
Flexible input power (AC/DC/DCC)
On board regulation to 12 vdc at NANO Vin
NANO itself produces the 5 VDC for sensors and servos
Header pins aligned with standard servo pinout
On board output driver chip can power small relays or actuators.
On board R680 current limiting resistors
2 board mounted Pushbuttons as DI’s
Prototype test area.
Bring out all unused digital and analog I/O
A dedicated header for I2C using A4/A5/+5 and Gnd
Spare I/O

## Slide 4: Introducing: MERGduino
Coming Soon

## Slide 5: MERGduino: Power Supply
Feature List (Power):
Flexible input power (AC / DCC or DC)
(OR 5 volts direct to Arduino)
On board regulation to 12 vdc at NANO Vin
Can be built standalone as a ‘power supply’ providing 12 volts.
Header pins to be provided on PCB for power take off.
On board LED for troubleshooting without NANO
Can learn to take measurements using DMM.
Feature List (DCC Opto-Coupler):
Optically couples DCC to Arduino Pin
Enables Arduino to act as a stationary Accessory decoder
Optional – Can omit if not needed. If it is used board must have an Arduino installed to provide the 5 volts for operation.

## Slide 6: MERGduino: I/O
Top Left
Standard I/O header with pins in order (Signal, 5VDC, Gnd)
Suitable for AI, AO, DI, DO with or without internal pullup
Top Right
Standard I/O header but with optional pullup resistor
Pullup is needed in at least one place on a I2C bus
Can also be used for precision voltage divider experiments
Middle
On Board buttons for I/O testing
For use with internal pullup
Includes current limiting resistor in case the pin is accidentally configured for output and then the button is pushed
Bottom
Optional LN2903 output driver.
If not used jumpers can be installed directly across.
If included allows a sinking current of 500 ma per pin. Can power small relays, incandescent bulbs, light strips.
4 on board LED’s with current limiting resistors for experimenting.
PCB to have pin headers so that LED’s could be remote mounted as signals, building lighting, mimic panel
Unused pins to have connection points available

## Slide 7: MERGduino: CPU
Standard NANO V3 Clone
To be mounted in header pins which are soldered onto the main board
optoisolator and other small components will be under the NANO
All I/O pins land somewhere and are available
PWM pins called out especially for use on SERVO’s or Motor control
I2C (SDA/SCL) have provision for pull up resistors otherwise same as standard analog pins
I2C brought out to 4 pin header for connection to servo expander
Tx/Rx available on 3 pin header
Still considering:
A row of holes where a DfPlayer ‘daughter board’ (MP3 sound effects) could be added.

## Slide 8: Links and Resources
https://rudysarduinoprojects.wordpress.com/2019/05/06/fun-with-arduino-29-dcc-accessory-decoder/
http://trainelectronics.com/DCC_Arduino/index.htm