## Slide 1: Arduino Class Programming with Examples
An Introduction
Alan Lomax
M8640

## Slide 2: Agenda
Motivation
Ground Work – Types and Structures
Basic Concepts - What is a Class ? How does it work?
Sample Code Fragments
Example Code
How and Why use a Class?
Inspecting the LED2 Class in Detail
Notes: Introduce Self!
Classes are a fundamental part of Object Oriented Programming.
Over the course of this talk we will be building on some concepts introduced previously.
There will be some learning of course .. But the main objective here is to inspire you to with your Arduino Programming.
Review Agenda

## Slide 3: Motivation
Part 1

## Slide 4: My Motivation
Notes: Show people that this can be about modelling on railways.
It is not just deep in the weeds Arduino programming.

## Slide 5: My Motivation
Notes: User interface – 5 buttons .. One speed control potentiometer one LCD screen (6 regions) showing 6 different status items, and 3 LED’s for when turntable bridge is in a specific position.
Other Inputs – 3 HALL effect sensors on outside of turntable well … detect micro magnets attached to bridge.
Other outputs – DC motor control direction and speed control.
Logic – depending on button press move in the correct direction until hall effect sensor is detected.

## Slide 6: Ground Work - Types and Structures
Part 2

## Slide 7: Ground Work
Variable Types
  int, bool, string, float, char[] (and others)
  Underneath all of these it is just bits and bytes of binary code
  When we declare a type we tell the compiler how to interpret the binary
  This is ‘bread and butter’ for programming in Arduino (and C++)
  int x = 5; // normally a 16 bit integer
  bool isPlaying = false; // a Boolean is true/false
  String fname = “Fred”; // a string represents text
Notes: Fundamentals to build on
When we talk about a variable Type … know what that is referring to.

## Slide 8: Types and Structures
struct (short for structure)
  It is possible (and not uncommon) to define our own variable type which is a combination of the basic types given previously. A simple example:
  struct structname {
  String fname;
  String lname;
  };
  structname fullName; // As with normal types you declare a new variable of this new type
  After defining the variable you can pass around the whole structure
  as fullName or refer to the individual component parts like this:
  fullName.fname = “Fred”
  fullName.lname = “Flintstone”
  int x; // for comparison a simple type declaring a new variable the same way
Notes: Structures are commonly used to handle related data as though it were a single item.
Not restricted to just two strings as shown .. Could be int, float etc. One structure could have many different component parts
Next page talks about Chris Sharp’s presentations over the past few MERG sessions

## Slide 9: Types and Structures
In a recent MERG Arduino SIG meeting Chris Sharp gave a presentation on structures and in particular focusing on a Servo structure he designed.
As the concept of structures was introduced it became clear that at a high level the code would be easier to maintain and develop.
But also the ‘code complexity’ was still in plain view.
(It was in essence just a reorganizing of existing code.)
Notes: I recall Chris using color coding to show at a high level how blocks of code were moved around.

## Slide 10: Basic Concepts - What is a Class ? - How does it work?
Part 3

## Slide 11: New Concept: A software Class
A class:
Very similar to a struct{ } a Class can be thought of as a user defined type … but the difference is it hides the implementation details.
This also means it hides complexity
To use a class you don’t need to know the implementation details
But we want to know!
All of this to be covered …. So lets go!
Notes: Using a class means you interact with it according to the authors wishes only.

## Slide 12: A Software Class
Led2
Class Definition
output
on
off
1 – Define a Class
Objects:
myLed1
myLed2
myLed3
2 – Create objects using the class definition.
3 – Use each of the objects thus created independently.
Notes: The class is called LED2 because it was my second go at it.
Do not be confused by the objects … they could be called anything we like … myLed1 .. myLed2 … myLed3 are just arbitrary names.

## Slide 13: Basic Concepts
Led2
Class Definition
Complexity may be hidden inside the shoebox
(But as a user we don’t care)
The class definition determines what ‘Properties & Methods’ are available in each of the objects we have created.
Complex Stuff
output
on
off

## Slide 14: LED2 is just an Example (We could be talking about a servo class)
Servo
Class Definition
Output Pin
Attach
Detach
Objects:
myServo1
myServo2
myServo3
Create ‘Servo’ objects using the class definition.
And use each of the objects thus created independently.
Write
Output Pin
Output Pin
Output Pin
Notes: The Picture hardly changes.

## Slide 15
The Next Train Departs in:
Notes: Using this PowerPoint break timer
This PowerPoint slide uses images, custom animation, and timing to provide a countdown timer that you can use in any presentation. When you open the template, you’ll notice that the timer is set at 00:00. However, when you start the slide show, the timer will start at the correct time and count down by 1-minute intervals until it gets to 1 minute. At that point, it will count down in two 30-seconds intervals to 00:00.
To insert this slide into your presentation
Save this template as a presentation (.ppt file) on your computer.
Open the presentation that will contain the timer.
On the Slides tab, place your insertion point after the slide that will precede the timer. (Make sure you don't select a slide. Your insertion point should be between the slides.)
On the Insert menu, click Slides from Files.
In the Slide Finder dialog box, click the Find Presentation tab.
Click Browse, locate and select the timer presentation, and then click Open.
In the Slides from Files dialog box, select the timer slide.
Select the Keep source formatting check box. If you do not select this check box, the copied slide will inherit the design of the slide that precedes it in the presentation.
Click Insert.
Click Close.

## Slide 16: Sample Code Fragments
Part 4

## Slide 17: Going a little Deeper
LED2
Class Definition
Name of our New Object
A passed parameter to be used when first constructing the object
#include "Led2.h"
Led2 myLed1 = Led2(13);
myLed1
Name of our Class
The header lets our sketch and the compiler know what is coming further down in the code.
- How to use the Led2 class to make a new object
- What properties and methods it has.
Pin 13
Led2 myLed1 = Led2(13);
A class definition is in at least two parts
- a header file (*.h) and
- a C++ program (*.CPP)
Notes: Note the definition is written as "LED2 myLed1 = LED2(13);“
This makes it easier to see the relationship with definition of a normal variable like "int pin = 13;" that the audience are familiar with.
Here is where it is useful to think of LED2 as a type (mentioned in (2) above.)
"LED2 myLed1(13);" does the same thing (generates the same code) but the assignment is not explicitly shown.

## Slide 18: A peek Under the Covers : The Constructor
Led2 Class
Led2 myLed1 = Led2(13);
This line is calling the constructor (It constructs the object we will want to use.)
Led2::Led2(byte pin) {
_pin = pin; // Save the passed pin
pinMode(_pin, OUTPUT); // define our output pin
off(); // call the off function
}
Inside the class definition this is what it does.
Notes: Key point – every time we call the constructor a ‘new’ object is created and all of the internal class variables for one object are separate from any other object of same class.
Explain my naming convention – variables inside a class have the leading underscore
I hope people are underwhelmed with this … the constructor is setting some internal values and the pinMode. We are not actually setting the output (yet).
Note the definition is written as "LED2 myLed1 = LED2(13);“
This makes it easier to see the relationship with definition of a normal variable like "int pin = 13;" that the audience are familiar with.
Here is where it is useful to think of LED2 as a type (mentioned in (2) above.)
"LED2 myLed1(13);" does the same thing (generates the same code) but the assignment is not explicitly shown.

## Slide 19: A peek Under the Covers : the on() property
Led2 Class
“on” Command
myLed1.on(); // Outside the shoebox use the on method of myLed1 object
void Led2::on() {
_blink = false; // Turn off blink mode
_state = HIGH; // Set desired state LED will turn on with next call to update
}
on() is a function within the class definition that sets the private internal variable _state and _blink
Notes: I hope people are underwhelmed with this … the on property is setting internal values but not actually doing anything to the LED output.

## Slide 20: Side discussion - File Locations
The header defines the ‘entry points’ for the functions but it is the CPP program that implements the functions. Both are required.
On the previous slide I indicated you would add the following line:
The use of angle brackets (<>) causes the compiler to search the default include directory. Using double quotes ("") causes it to search the current working directory and only if that search fails the default include directory.
#include "Led2.h"
But where do the *.h and *.cpp files actually go?
If you use “double quotes” (as shown above) then put the two files in same directory as your main sketch. This is good while developing or testing.
If you use <angle brackets> then the two files must go in your libraries folder (under the folder where you keep your sketches.)
This is good for your final class code.

## Slide 21: Example Code
Part 5

## Slide 22: The Header File
A class definition is in at least two parts
- a header file (*.h) and
- a C++ program (*.CPP)
/*****************************************************
** LED2_H **
** **
** This class implements standard LED on-off **
** logic on a pin you specify plus a configurable **
** blinking effect. It does so without any delay **
** calls. (no blocking code) **
*****************************************************
*/
class Led2 {
private:
int _pin; // the number of the LED pin
unsigned long _onTime; // milliseconds of on-time
unsigned long _offTime; // milliseconds of off-time
unsigned long _nextTime; // next time change in milliseconds
bool _blink; // true if we are in blinking mode, false if not
{ snip }
public:
Led2(byte pin); // Simple default definition
void update(); // update things based on elapsed time (call often)
void off(); // Turning off the LED (and sets blink to false)
void on(); // Turning on the LED (and sets blink to false)
{ snip }
};
Tell compiler we are defining a class
Some variables (or functions) are private – completely inside the shoebox
Some are public – available outside the class sticking out of the shoebox
This function has same name as class and no other return type – it is the CONSTRUCTOR
This (incomplete) code is the header. Notice It tells the compiler what to expect in the CPP program … but it has no real executable code of its own.
Notes: For simplicity and to fit the page some lines have been snipped out.
For the complete solution go to the GitHub page.

## Slide 23: The C++ part
A class definition is in at least two parts
- a header file (*.h) and
- a C++ program (*.CPP)
#include "Led2.h"
Led2::Led2(byte pin) {
// Save the passed pin
_pin = pin;
init();
}
void Led2::init() {
pinMode(_pin, OUTPUT); // define our output pin
off(); // call the function that sets out LED to off initially
}
void Led2::off() {
_blink = false; // Turn off blink mode
_state = LOW; // Set the desired state - LED will turn off on next call to update
}
void Led2::on() {
_blink = false; // Turn off blink mode
_state = HIGH; // Set desired state LED will turn on with next call to update
}
void Led2::update() {
if (_blink) { // If in blinking mode look at timing first
if ( millis() >= _nextTime) { // It is time to do something.
_nextTime = millis() + (_state == LOW ? _onTime : _offTime); // and calculate when next
// change of state is due
_state = !_state; // swap states
}
}
digitalWrite(_pin, _state); // update the actual output according to desired state
}
Include the header
Here is our CONSTRUCTOR (name is same as class name). We pass it pin and all it does is save it in a private variable called _pin
Then call a separate function to initialize things.
The separate function to initialize things is itself dirt simple .. It sets the pinMode and calls yet another function called off()
The separate functions on() and off() just set two internal variables.
Note that at no point so far have we actually written anything to the output.
The Magic Sauce. A public method called update. If blink is true it checks if it is time to swap states .. Otherwise carry on. And finally write the _state to the _pin
Note: No delays, no blocking code. Update executes very quickly.
Led2 myLed1 = Led2(13);
myLed1.on();
myLed1.update();
Notes: The public functions are what the outside world (ie your main program) sees.
All of the internal code is hidden complexity.
Most of the methods (or functions if you prefer) just get or set internal variables. In quick and get out.
The update method reads and acts on the internal variables … typically it is doing most of the work.

## Slide 24: In your Main Program
#include <Led2.h>
Led2 myLed1 = Led2(13);
void setup() {
myLed1.onTime(50); // Set LED onTime (50 ms)
myLed1.offTime(300); // Set LED offTime (300 ms)
myLed1.blink(); // turn on blink mode
}
void loop()
{
myLed1.update(); // call update frequently
}
Defining it before setup makes myLed1 a global variable. It can be accessed in setup or in loop code.
In setup configure any settings we want.
Loop code could not be simpler. The work is done inside the class checking millis() and doing the work.

## Slide 25: Summary: How it all works together
1) Use The class definition and create an object like so:
LED2 myLed1 = LED2(13);
2) constructor runs and sets private (internal to class) variables:
_pin = 13, _state=OFF
and the mode of _pin is set to OUTPUT
LED2
Class Definition
output
on
off
update
Object
myLed1
_pin = 13
_state = OFF
pinMode(_pin, OUTPUT);
13
on
off
update
5) When next our loop code calls myLed1.update() it will check the local variables _state and writes it to the output pin.
It is only at this point our LED will turn ON.
Object
myLed1
_pin = 13
_state = ON
13
on
off
update
4) Now lets say we called the on method myLed1.on() All this does is set the local variable _state to on. At this point still nothing happens because _state is just a private variable inside our class.
3) In loop code we call the update method myLed1.update() which executes the line digitalWrite(_pin, _state)
Not too much else happens- we just turned off a pin that was probably already off!

## Slide 26: How and Why use a Class?
Part 6

## Slide 27: Recapping The Key Points
LED2 Class Definition
LED2 myLed1(13);
myLed1 Object
Key Point #1:
The object is defined by the class but is separate.
You do not need to know the inner workings of the class definition in order to use it.
LED2 myLed2(5);
LED2 myLed3(6);
LED2 myLed4(7);
myLed2,3,4 Objects
Key Point #2: Although each of the objects gets its functionality from the same class definition, each object is independent and the objects do not interact .
Key Point #4: There is no such thing as magic!
Key Point #3: Reusability of class creating multiple objects that behave the same without exposing the complexity makes for coding efficiency.

## Slide 28
The Next Train Departs in:
Notes: Using this PowerPoint break timer
This PowerPoint slide uses images, custom animation, and timing to provide a countdown timer that you can use in any presentation. When you open the template, you’ll notice that the timer is set at 00:00. However, when you start the slide show, the timer will start at the correct time and count down by 1-minute intervals until it gets to 1 minute. At that point, it will count down in two 30-seconds intervals to 00:00.
To insert this slide into your presentation
Save this template as a presentation (.ppt file) on your computer.
Open the presentation that will contain the timer.
On the Slides tab, place your insertion point after the slide that will precede the timer. (Make sure you don't select a slide. Your insertion point should be between the slides.)
On the Insert menu, click Slides from Files.
In the Slide Finder dialog box, click the Find Presentation tab.
Click Browse, locate and select the timer presentation, and then click Open.
In the Slides from Files dialog box, select the timer slide.
Select the Keep source formatting check box. If you do not select this check box, the copied slide will inherit the design of the slide that precedes it in the presentation.
Click Insert.
Click Close.

## Slide 29: Inspecting the LED2 Class in detail
Part 7

## Slide 30: The full Led2 class
LED2 Class
Output (Pin)
“on” Command
“off” Command
On and Off commands are hardly a compelling usage case
“blink” Command
“onTime (ms)”
“offTime (ms)”
state (T / F)
A blink command for our class makes it a bit more interesting
“update()”
User definable on time and off times - better
Blinking an LED output without ever calling delay() is an example of hidden complexity
As a user you don’t need to know how it works, only that it does work!
“update()”
Complexity is hidden inside the shoebox

## Slide 31: Live Demo Time
Single LED blinking
Multiple LEDs blinking with different patterns
Multiple LEDs blinking with different patterns and a Servo sweep
Notes: Share screen show code … load code wink over to second camera describe what people are seeing.
Change timing and show effect. Pause for discussion.
Look into class code – discuss how it works.
Move to next example.

## Slide 32: Going deeper with a code review….
LED2 Class
Lets take a look at and talk through the code:
Latest: https://github.com/Alan-Lomax/Led2
A snapshot also included later in this PPT.

## Slide 33: Some More Examples (+ Inspecting Class Programming)
DblDelay https://github.com/Alan-Lomax/DblDelay
Timer https://github.com/Alan-Lomax/Timer
Button https://github.com/Alan-Lomax/Button
LCD2x20 https://github.com/Alan-Lomax/LCD_NHD2x20
LED2 https://github.com/Alan-Lomax/Led2

## Slide 34: Recap
A blueprint for making software ‘objects’
A way of making re-usable software parts
A way of hiding complexity
A user defined variable type
A fundamental part of Object Oriented Programming

## Slide 35
Questions?
Some Additional Reading follows
(If you are interested)

## Slide 36: Ground Work – Types and Structures
byte x = 65;
char myLetter = ‘A’;
In binary both of these are the same bit pattern 01000001
The computer does not care.
It is only how we interpret the two variables that matters.
  Lots of on line help is available (see references)

## Slide 37: Why use a Class?
Comprehension (details are hidden, code is easier to understand)
Productivity (defining and using an object can be very quick)
Portability (The same class can be used in many sketches)
Testability (Testing, isolating and debugging is compartmentalized)
Inheritance (New classes can build on other classes)

## Slide 38: Why Not use a Class?
For some applications they are not needed so why use a class to do what might be a trivial thing
Classes are still programs and programs do have bugs.
All that hidden complexity might represent a can of worms if you did not write the code but still need to dig into it.
There is a learning curve, especially if a class has lots of properties and methods.
Changing a class can have knock on effects to many programs that depend on it working a certain way

## Slide 39: Lessons Learned
IMO: The hardest part is knowing what properties and methods are available with a given (non-trivial) class.
Not only what they are but also the many options available for a given property can also be quite involved.
These aspects are often poorly documented. Realizing the true power of a class is a challenge under such conditions and users might be reluctant to accept the implementation at face value.
An example sketch demonstrating usage of some properties is helpful – but is not sufficient if there are many options and alternate uses.

## Slide 40: LED2.H
#ifndef MY_LED2_H
#define MY_LED2_H
#include "Arduino.h"
/*
*****************************************************
** LED2_H **
** **
** This class implements standard LED on-off **
** logic on a pin you specify plus a configurable **
** blinking effect. It does so without any delay **
** calls. (no blocking code) **
*****************************************************
*/
class Led2 {
private:
int _pin; // the number of the LED pin
long _onTime; // milliseconds of on-time
long _offTime; // milliseconds of off-time
bool _blink; // true if we are in blinking mode, false if not
int _state; // ledstate used to set the LED
unsigned long _previousMillis; // the last time LED was updated
void init(); // Initialization code
public:
Led2(byte pin); // Simple default definition without a pre specified on and off time.
Led2(byte pin, long on, long off); // this definition includes the on and off time values from the outset
void update(); // update things based on elapsed time (call this as often as possible)
bool getState(); // Return the current state of LED
bool getBlink(); // return the LEDs current blinking state (true / false)
void onTime(long on); // Set the onTime to a new value
long onTime(); // Return the current onTime
void offTime(long off); // Set the offTime to a new value
long offTime(); // Return the current offTime
void off(); // Set the On time to zero and the Off time to 500 - Turning off the LED
void on(); // Set the Off time to zero and the On time to 500 - Turning on the LED
void blink(); // set the LED to a blinking state using the previously set timing values
};
#endif

## Slide 41: LED2.CPP (1/3)
#include "Led2.h"
Led2::Led2(byte pin, long on, long off) {
// Save the passed pin and timing values into the equivalent local variables (with underscore)
_pin = pin;
_onTime = on;
_offTime = off;
// Initialization code is kept separate just for clarity.
init();
}
Led2::Led2(byte pin) {
// Save the passed pin
_pin = pin;
init();
}
void Led2::init() {
pinMode(_pin, OUTPUT);
// Initialize local variables for the new class member
_state = LOW; // start with LED on the off condition
_blink = false; // no blinking at initialization
off(); // call the function that sets out LED to off initially
}

## Slide 42: LED2.CPP (2/3)
void Led2::update() {
// check to see if it's time to change the state of the LED
unsigned long currentMillis = millis();
if (!_blink) { // If not in blinking mode just look at on or off conditions
if (_state == LOW) {
digitalWrite(_pin, LOW); // Turn off the actual LED.
}
else if (_state == HIGH) {
digitalWrite(_pin, HIGH); // Turn on the actual LED.
}
}
else { // We are in blinking mode so cycle accordingly
if ((_state == HIGH) && (currentMillis - _previousMillis >= _onTime)) {
_state = LOW; // Turn it off
_previousMillis = currentMillis; // Remember the time
}
else if ((_state == LOW) && (currentMillis - _previousMillis >= _offTime)) {
_state = HIGH; // turn it on
_previousMillis = currentMillis; // Remember the time
}
digitalWrite(_pin, _state); // update the actual LED.
}
}
bool Led2::getState() {
// return the current state of the led (True or False)
return _state;
}
bool Led2::getBlink() {
// return the current blink state of the led (True or False)
return _blink;
}
void Led2::onTime(long on) {
// update the desired on time of the led
_onTime = on;
}

## Slide 43: LED2.CPP (3/3)
long Led2::onTime() {
// return the current on time of the led
return _onTime;
}
void Led2::offTime(long off) {
// update the desired off time of the led
_offTime = off;
}
long Led2::offTime() {
// return the current off time of the led
return _offTime;
}
void Led2::off() {
_blink = false; // Turn off blink mode
_state = LOW; // Set the desired state - LED will turn off on next call to update
}
void Led2::on() {
_blink = false; // Turn off blink mode
_state = HIGH; // Set the desired state - LED will turn on on next call to update
}
void Led2::blink() {
_blink = true; // Turn on blink mode
// Set the desired state - LED will start blinking as of next call to update
}

## Slide 44
References and Additional Material
Binary numbers and types :
http://users.ece.utexas.edu/~valvano/embed/chap3/chap3.htm
Alternate explanations on subject of Classes:
https://www.guru99.com/cpp-classes-objects.html
http://mypractic.com/lesson-7-classes-in-c-language-for-arduino-button-as-an-object/
https://www.geeksforgeeks.org/c-classes-and-objects/
http://paulmurraycbr.github.io/ArduinoTheOOWay.html