## Slide 1: Arduino Class Programming with Examples
An Introduction
Alan Lomax
M8640

## Slide 2: Agenda
Ground Work – Types and Structures
Basic Concepts - What is a Class ? How does it work?
How and Why use a Class?
Some Example Code snippets
Inspecting the LED2 Class in some detail

## Slide 3: Laying the Ground Work – Types and Structures
Variable Types
  int, string, float, char[], bool and others
  Underneath all of these it is just bytes of binary code
  When we declare a type we tell the compiler how to interpret the binary
  These are the ‘bread and butter’ concepts
  int x = 5; // normally a 16 bit integer
  bool isPlaying = false; // a Boolean is true/false
  String fname = “Fred”; // a string represents text
  Lots of on line help is available (see references)

## Slide 4: Laying the Ground Work – Types and Structures
struct = short for structure
  It is possible (and not uncommon) to define our own variable type which is some combination of the basic types given previously. A simple example:
  struct name {
  String fname;
  String lname;
  };
  name fullName; // Just like with the other types you declare a new variable using our new type
  And after that you can pass around the whole structure or
  refer to the individual component parts like this:
  fullName.fname = “Fred”
  fullName.lname = “Flintstone”
  Commonly use structures to handle related data as if it were a single item.

## Slide 5: Laying the Ground Work – Types and Structures
In a recent MERG Arduino SIG Chris Sharp gave a presentation on structures and in particular focusing on a Servo structure. (You may recall it.)
Because structures were used at a high level the code was reorganized and easier to maintain and grow … but the ‘complexity’ was still in plain view.
Enter …. classes

## Slide 6: Basic Concepts: What is a Class ?
A class:
Very similar to a struct{ } but can hide implementation details
This also means it is a way of hiding complexity
It too can be thought of as a user defined type
As a ‘type’ it is also a blueprint for making software ‘objects’ which is a way of making re-usable software parts
And yes ..
Classes are a fundamental part of Object Oriented Programming
All of this to be covered ….

## Slide 7: Basic Concepts
LED2
Class Definition
output
on
off
1 – Define a Class
Objects:
myLed1
myLed2
myLed3
2 – Create objects using the class definition.
3 – Use each of the objects thus created independently.

## Slide 8: LED2 is just an Example We could be talking about a servo class
Servo
Class Definition
Output Pin
Attach
Detach
Objects:
myServo1
myServo2
myServo3
Create ‘Servo’ objects using the class definition.
And use each of the objects thus created independently.
Write
Output Pin
Output Pin
Output Pin

## Slide 9: Basic Concepts
LED2
Class Definition
Complexity may be hidden inside
(But we don’t care)
The class definition determines what ‘Properties & Methods’ are available in each of the objects we have created.
Complex Stuff
output
on
off
The objects can interact with hardware (eg: LED on/off, Servo going to a position)

## Slide 10: A peek Under the Covers : the on() property
LED2 Class
“on” Command
myLed1.on();
void Led2::on() {
_blink = false; // Turn off blink mode
_state = HIGH; // Set desired state LED will turn on with next call to update
}
On() is a function within the class definition that sets the private internal variable _state and _blink

## Slide 11: Going a little Deeper
LED2
Class Definition
Name of our New Object
A passed parameter to be used when first constructing the object
#include "Led2.h“
LED2 myLed1 = LED2(13);
myLed1
Name of our Class
The header lets our sketch and the compiler know what is coming further down in the code.
- How to use the LED2 class to make a new object
- What properties and methods it has.
Pin 13
LED2 myLed1 = LED2(13);
A class definition is in at least two parts
- a header file (*.h) and
- a C++ program (*.CPP)
Notes: Note the definition is written as "LED2 myLed1 = LED2(13);“
This makes it easier to see the relationship with definition of a normal variable like "int pin = 13;" that the audience are familiar with.
Here is where it is useful to think of LED2 as a type (mentioned in (2) above.)
"LED2 myLed1(13);" does the same thing (generates the same code) but the assignment is not explicitly shown.

## Slide 12: The Header File
A class definition is in at least two parts
- a header file (*.h) and
- a C++ program (*.CPP)
/*****************************************************
** LED2_H **
** **
** This class implements standard LED on-off **
** logic on a pin you specify plus a configurable **
** blinking effect. It does so without any delay **
** calls. (no blocking code) **
*****************************************************
*/
class Led2 {
private:
int _pin; // the number of the LED pin
unsigned long _onTime; // milliseconds of on-time
unsigned long _offTime; // milliseconds of off-time
unsigned long _nextTime; // next time change in milliseconds
bool _blink; // true if we are in blinking mode, false if not
{ snip }
public:
Led2(byte pin); // Simple default definition
void update(); // update things based on elapsed time (call often)
void off(); // Turning off the LED (and sets blink to false)
void on(); // Turning on the LED (and sets blink to false)
{ snip }
};
#endif
Tell compiler we are defining a class
Some variables (or functions) are private – only available inside the class
Some are public – available outside the class
This function has same name as class and no other return type – it is the CONSTRUCTOR
Notes: Note the definition is written as "LED2 myLed1 = LED2(13);“
This makes it easier to see the relationship with definition of a normal variable like "int pin = 13;" that the audience are familiar with.
Here is where it is useful to think of LED2 as a type (mentioned in (2) above.)
"LED2 myLed1(13);" does the same thing (generates the same code) but the assignment is not explicitly shown.

## Slide 13: The C++ part
A class definition is in at least two parts
- a header file (*.h) and
- a C++ program (*.CPP)
#include "Led2.h"
Led2::Led2(byte pin) {
// Save the passed pin
_pin = pin;
init();
}
void Led2::init() {
pinMode(_pin, OUTPUT); // define our output pin
off(); // call the function that sets out LED to off initially
}
void Led2::off() {
_blink = false; // Turn off blink mode
_state = LOW; // Set the desired state - LED will turn off on next call to update
}
void Led2::update() {
if (_blink) { // If in blinking mode look at timing first
if ( millis() >= _nextTime) { // It is time to do something.
_nextTime = millis() + (_state == LOW ? _onTime : _offTime); // and calculate when next
// change of state is due
_state = !_state; // swap states
}
}
digitalWrite(_pin, _state); // update the actual output according to desired state
}
Include the header
Here is our CONSTRUCTOR (name is same as class name). We pass it pin and all it does is save it in a private variable called _pin
Then call a separate function to initialize things.
The separate function to initialize things is itself dirt simple .. It sets the pinMode and calls yet another function called off()
The separate function off() just sets two internal variables.
Note that at no point so far have we actually written anything to the output.
The Magic Sauce. A public method called update. If blink is true it checks if it is time to swap states .. Otherwise carry on. And finally write the _state to the _pin
Note: No delays, no blocking code. Update executes very quickly.
Notes: The public functions are what the outside world (ie your main program) sees.
All of the internal code is hidden complexity.
Most of the functions (or methods if you prefer) just get or set internal variables.
The update method reads and acts on the internal variables … typically doing most of the work.

## Slide 14: In your Main Program
#include <Led2.h>
Led2 myLed1 = Led2(13);
void setup() {
myLed1.onTime(50); // Set LED onTime (50 ms)
myLed1.offTime(300); // Set LED offTime (300 ms)
myLed1.blink(); // turn on blink mode
}
void loop()
{
myLed1.update(); // call update frequently
}
Defining it before setup makes myLed1 a global variable. It can be accessed in setup or in loop code.
In setup configure any settings we want.
Loop code could not be simpler. The work is done inside the class checking millis() and doing the work.

## Slide 15: How it all works together
1) Use The class definition and create an object like so:
LED2 myLed1 = LED2(13);
2) constructor runs and sets local variables _pin = 13, _state=OFF
It then sets the mode of _pin to OUTPUT
LED2
Class Definition
output
on
off
update
Object
myLed1
_pin = 13
_state = OFF
pinMode(_pin, OUTPUT);
13
on
off
update
5) When next our loop code calls myLed1.update() it will check the local variables _state and writes it to the output pin.
It is only at this point our LED will turn ON.
Object
myLed1
_pin = 13
_state = ON
13
on
off
update
4) Now lets say we called the on method myLed1.on() All this does is set the local variable _state to on. At this point still nothing happens because _state is just a private variable inside our class.
3) In loop code we call the update method myLed1.update() which executes the line digitalWrite(_pin, _state)
Not too much else happens- we just turned off a pin that was probably already off!

## Slide 16: Where are we At ?
LED2 Class
Output (Pin)
“on” Command
“off” Command
Lets be honest! On and Off commands are hardly a compelling usage case so far!
(We can do that much by writing directly to the output with digitalWrite(13, HIGH) )
“blink” Command
“onTime (ms)”
“offTime (ms)”
state (T / F)
A blink command for our class sounds a bit more interesting
“update()”
How about blink with a user definable on time and off time?
And blinking an LED output without ever calling delay() is an example of hidden complexity
As a user you don’t really need to know how it works, only that it does work!
But after a quick recap let’s put on a programmer hat and dig deeper still ….
“update()”

## Slide 17: Recapping The Key Points
LED2 Class Definition
LED2 myLed1(13);
myLed1 Object
Key Point #1:
The object is defined by the class but is separate.
You do not need to know the inner workings of the class definition in order to use it.
LED2 myLed2(5);
LED2 myLed3(6);
LED2 myLed4(7);
myLed2,3,4 Objects
Key Point #2: Although each of the objects gets its functionality from the same class definition, each object is independent and the objects do not interact .
Key Point #3: There is no such thing as magic!

## Slide 18: Going deeper with a code review….
LED2 Class
Lets take a look at and talk through the code:
Latest: https://github.com/Alan-Lomax/Led2
A snapshot also included later in this PPT.

## Slide 19: My Motivation

## Slide 20: My Motivation

## Slide 21: Some More Examples (+ Inspecting Class Programming)
DblDelay https://github.com/Alan-Lomax/DblDelay
Timer https://github.com/Alan-Lomax/Timer
Button https://github.com/Alan-Lomax/Button
LCD2x20 https://github.com/Alan-Lomax/LCD_NHD2x20
LED2 https://github.com/Alan-Lomax/Led2

## Slide 22: Recap
A blueprint for making software ‘objects’
A way of making re-usable software parts
A way of hiding complexity
A user defined variable type
A fundamental part of Object Oriented Programming

## Slide 23
Questions?
Some Additional Reading follows
(If you are interested)

## Slide 24: Why use a Class?
Comprehension (details are hidden, code is easier to understand)
Productivity (defining and using an object can be very quick)
Portability (The same class can be used in many sketches)
Testability (Testing, isolating and debugging is compartmentalized)
Inheritance (New classes can build on other classes)

## Slide 25: Why Not use a Class?
For some applications they are not needed so why use a class to do what might be a trivial thing
Classes are still programs and programs do have bugs.
All that hidden complexity might represent a can of worms if you did not write the code but still need to dig into it.
There is a learning curve, especially if a class has lots of properties and methods.
Changing a class can have knock on effects to many programs that depend on it working a certain way

## Slide 26: Lessons Learned
IMO: The hardest part is knowing what properties and methods are available with a given (non-trivial) class.
Not only what they are but also the many options available for a given property can also be quite involved.
These aspects are often poorly documented. Realizing the true power of a class is a challenge under such conditions and users might be reluctant to accept the implementation at face value.
An example sketch demonstrating usage of some properties is helpful – but is not sufficient if there are many options and alternate uses.

## Slide 27: LED2.H
#ifndef MY_LED2_H
#define MY_LED2_H
#include "Arduino.h"
/*
*****************************************************
** LED2_H **
** **
** This class implements standard LED on-off **
** logic on a pin you specify plus a configurable **
** blinking effect. It does so without any delay **
** calls. (no blocking code) **
*****************************************************
*/
class Led2 {
private:
int _pin; // the number of the LED pin
long _onTime; // milliseconds of on-time
long _offTime; // milliseconds of off-time
bool _blink; // true if we are in blinking mode, false if not
int _state; // ledstate used to set the LED
unsigned long _previousMillis; // the last time LED was updated
void init(); // Initialization code
public:
Led2(byte pin); // Simple default definition without a pre specified on and off time.
Led2(byte pin, long on, long off); // this definition includes the on and off time values from the outset
void update(); // update things based on elapsed time (call this as often as possible)
bool getState(); // Return the current state of LED
bool getBlink(); // return the LEDs current blinking state (true / false)
void onTime(long on); // Set the onTime to a new value
long onTime(); // Return the current onTime
void offTime(long off); // Set the offTime to a new value
long offTime(); // Return the current offTime
void off(); // Set the On time to zero and the Off time to 500 - Turning off the LED
void on(); // Set the Off time to zero and the On time to 500 - Turning on the LED
void blink(); // set the LED to a blinking state using the previously set timing values
};
#endif

## Slide 28: LED2.CPP (1/3)
#include "Led2.h"
Led2::Led2(byte pin, long on, long off) {
// Save the passed pin and timing values into the equivalent local variables (with underscore)
_pin = pin;
_onTime = on;
_offTime = off;
// Initialization code is kept separate just for clarity.
init();
}
Led2::Led2(byte pin) {
// Save the passed pin
_pin = pin;
init();
}
void Led2::init() {
pinMode(_pin, OUTPUT);
// Initialize local variables for the new class member
_state = LOW; // start with LED on the off condition
_blink = false; // no blinking at initialization
off(); // call the function that sets out LED to off initially
}

## Slide 29: LED2.CPP (2/3)
void Led2::update() {
// check to see if it's time to change the state of the LED
unsigned long currentMillis = millis();
if (!_blink) { // If not in blinking mode just look at on or off conditions
if (_state == LOW) {
digitalWrite(_pin, LOW); // Turn off the actual LED.
}
else if (_state == HIGH) {
digitalWrite(_pin, HIGH); // Turn on the actual LED.
}
}
else { // We are in blinking mode so cycle accordingly
if ((_state == HIGH) && (currentMillis - _previousMillis >= _onTime)) {
_state = LOW; // Turn it off
_previousMillis = currentMillis; // Remember the time
}
else if ((_state == LOW) && (currentMillis - _previousMillis >= _offTime)) {
_state = HIGH; // turn it on
_previousMillis = currentMillis; // Remember the time
}
digitalWrite(_pin, _state); // update the actual LED.
}
}
bool Led2::getState() {
// return the current state of the led (True or False)
return _state;
}
bool Led2::getBlink() {
// return the current blink state of the led (True or False)
return _blink;
}
void Led2::onTime(long on) {
// update the desired on time of the led
_onTime = on;
}

## Slide 30: LED2.CPP (3/3)
long Led2::onTime() {
// return the current on time of the led
return _onTime;
}
void Led2::offTime(long off) {
// update the desired off time of the led
_offTime = off;
}
long Led2::offTime() {
// return the current off time of the led
return _offTime;
}
void Led2::off() {
_blink = false; // Turn off blink mode
_state = LOW; // Set the desired state - LED will turn off on next call to update
}
void Led2::on() {
_blink = false; // Turn off blink mode
_state = HIGH; // Set the desired state - LED will turn on on next call to update
}
void Led2::blink() {
_blink = true; // Turn on blink mode
// Set the desired state - LED will start blinking as of next call to update
}

## Slide 31
References and Additional Material
Binary numbers and types :
http://users.ece.utexas.edu/~valvano/embed/chap3/chap3.htm
Alternate explanations on subject of Classes:
https://www.guru99.com/cpp-classes-objects.html
http://mypractic.com/lesson-7-classes-in-c-language-for-arduino-button-as-an-object/
https://www.geeksforgeeks.org/c-classes-and-objects/
http://paulmurraycbr.github.io/ArduinoTheOOWay.html