## Slide 1: Practical Arduino
From the Ground Up

## Slide 2: Outline (assumes no Prior electronics or Arduino knowledge)
Review Design Objectives. What you will learn. What you will need. Primer on Components and Symbols. Conductors, Insulators and Ohms Law. Introduce the kit and the included parts and how to obtain one.
Schematic vs PCB. Start it simple. Work up to this design complete walkthrough. (parts orientation, details, tips and tricks, how to solder, assemble board.) Build up the power supply portion the board. How to test your work with visual inspection and basic electrical testing.
Finish the build. Introduce The Arduino IDE. Use of in built test programs like Blink, Servo etc
More on Arduino IDE and simple program design. Use of serial monitor for debugging. Examples of practical use (Each as a standalone short video)
  LED outputs (timing and random light)
  Button Inputs (debouncing and controlling program flow)
  Infrared detectors (sensor needed)
  LDR sensors (LDR needed)
  Motor Control (Motor Shield needed)
  LCD displays (LCD display needed)

## Slide 3: General Requirements
Basis:
An Arduino based hardware and software project that will serve as a learning platform
Finished product very useful in a variety of situations on any layout.
Ideally ordered a kit complete with the Arduino NANO (clone)
PCB design should be flexible in that I/O can be reconfigured without too much fuss. (for example taking the LED’s off board)
A series of videos can be made for self paced learning (able to pause, go back, review and check)
No expectation of ‘live sessions’ other than maybe introducing the kit once it is available
NANO V3 MCU
Carrier Board
4 LED on board via R680
2 SERVO via 3pin Header
I2C via A4/A5
2 Buttons on board
DCC signal via optocoupler
4 Sensors via 3 pin header
AC/DC or DCC powered
ULN2803A Output Driver
Feature List:
Socketable NANO on a carrier board.
Carrier board itself has mounting holes.
Flexible power AC/DC/DCC regulated to 12 vdc at NANO Vin
NANO itself produces the 5 VDC for sensors and servos
Header pins to align with standard servo pinout
On board R680/R1K current limiting resistors
2 board mounted Pushbuttons as DI’s
Prototype test area.
Bring out unused digital and analog I/O
A dedicated header for I2C using A4/A5/+5 and Gnd
Pull up resistors for LDR and I2C usage.
It may be that not all I/O is usable at the same time but that would be the going in objective
Spare I/O